OALCF Task Cover Sheet

Task Title: Calculate Angles

| Learner Name: |
| --- |
| Date Started: Date Completed: Successful Completion: Yes___ No___ |
| Goal Path: Employment ( Apprenticeship ( Secondary School Post Secondary Independence___ |
| Task Description: Carpenters calculate angles to construct trusses and stairs |
| Competency: A: Find and Use Information C: Understand and Use Numbers D: Use Digital technology | Task Group(s): A2: Interpret documents C1: Manage money C3: Use measures |
| Level Indicators: A1.2: Read texts to locate and connect ideas and information A2.1: Interpret very simple documents to locate specific details A2.2: Interpret simple documents to locate and connect information C1.2: Make low-level inferences to calculate costs and expenses that may include rates such as taxes and discounts C3.3: Use measures to make multi-step calculations; use specialized measuring tools D.2: Perform well-defined, multi-step digital tasks |
| Performance Descriptors: see chart on last page |
| Materials Required: Pencil Calculator ANGLES DRAWINGS document |

Task Title: Calculate Angles

Carpenters use calculators and formulas to calculate angles to meet safety regulations and to determine amounts of material required.

Learner Information and Tasks:

Review the ANGLES DRAWINGS document.

All measurement answers are to be in feet or decimals of feet.

Carpenters use the a2 + b2 = c2 formula to calculate lengths of stairs and stringers (c) where a = height or rise and b = length or run.

Rise (a)		Length of Stair/Stringer (c)

Run (b)

Task 1:	Look at the diagram labelled ‘LADDER’ from the ANGLE DRAWINGS document.  Calculate the range of allowable distance between the wall and the bottom of the ladder when the ladder is not securely fastened, according to the LADDERS Section of the Ontario Health and Safety Act.

Task 2:	Look at the diagram labelled ‘TRUSS’ from the ANGLE DRAWINGS document.

- Calculate the length of the remaining sides of the truss.

- If 2X4 lumber is 36¢/linear foot, plus HST, how much will the lumber cost for the truss?

Task 3:	A staircase is to be built from the second floor of the house to the patio.  The staircase will join the second floor deck twelve feet above the ground and rest on the patio nine feet from the house.

How long will each stringer be?

Occupational Health and Safety Act

ONTARIO REGULATION 67/93

HEALTH CARE AND RESIDENTIAL FACILITIES

83.  When a ladder is being used it shall,

(a) be placed on a firm footing and secured against slipping;

(b) if the ladder is between six and nine metres in length, be securely fastened or be held in place by one or more workers while being used;

(c) if the ladder exceeds nine metres in length, be securely fastened or stabilized to prevent it from tipping or falling;

(d) when not securely fastened, be inclined so that the horizontal distance from the top support to the foot of the ladder is not less than one-quarter and not more than one-third of the length of the ladder; and

(e) if the ladder is likely to be endangered by traffic, have a worker stationed at its foot to direct such traffic or have barriers or warning signs placed at its foot. O. Reg. 67/93, s. 83.

Internet, November 17, 2013.

Task Title: Calculate Angles

Answer Key

Task 1:	The carpenter scans the Section of the Act presented; locates the reference to a ladder “not securely fastened”.  The carpenter scans the ‘Ladder’ diagram on the Angle Drawings document to determine the height of the ladder (from the ground to its resting place).

The distance of the foot of the ladder from the wall must be at least ¼ of the height but not more than 1/3 of the height.

Height = 8’

Distance = ¼ x 8’ = 2’ (minimum)

Distance = 1/3 x 8’ = 2.7’

The distance between the wall and the bottom of the ladder must be at least 2’ but not more than 2.7’.

Task 2:	a) a2 + b2 = c2, where a = 6’ and b = 24/2 = 12’

62 + 122 = c2

36 + 144 = c2

180 = c2

13.42’ = c

The truss will require one length of a (6’), two lengths of b (2 x 12’ = 24’) and two lengths of c (2 x 13.42’ = 26.84’).

- Total amount of lumber = 6’ + 24’ + 26.84’

Total amount of lumber = 56.84’

Total cost of lumber = 56.84’ x 36¢ + HST

Total cost of lumber = $20.46 + ($20.46 x .13)

Total cost of lumber = 20.46 x $2.66

Total cost of lumber = $23.12

Task 3:	a2 + b2 = c2 where a = height and b = length

122 + 92 = c2

144 + 81 = c2

225 = c2

15 = c

Each stringer will be 15’ long.

## Task Title: Calculate Angles

| Performance Descriptors | Needs Work | Completes task with support from practitioner | Completes task independently |
| --- | --- | --- | --- |
| A1.2 | scans text to locate information |  |  |  |
|  | locates multiple pieces of information in simple texts |  |  |  |
|  | makes low-level inferences |  |  |  |
|  | reads more complex texts to locate a single piece of information |  |  |  |
| A2.1 | scans to locate specific details |  |  |  |
|  | interprets brief text and common symbols |  |  |  |
|  | locates specific details in simple documents, such as labels and signs |  |  |  |
| A2.2 | performs limited searches using one or two search criteria |  |  |  |
|  | locates information in simple graphs and maps |  |  |  |
|  | makes low-level inferences |  |  |  |
| C1.2 | calculates using numbers expressed as whole numbers, fractions, decimals, percentages and integers |  |  |  |
|  | calculates percentages |  |  |  |
|  | interprets and applies rates (e.g. $/kg, $/1) |  |  |  |
|  | chooses and performs required operation(s); may make inferences to identify required operation(s) |  |  |  |
|  | selects appropriate steps to reach solutions |  |  |  |
|  | represents costs and rates using monetary symbols, decimals and percentages |  |  |  |
|  | interprets, represents and converts amounts using whole numbers, decimals, percentages, ratios and simple, common fractions (e.g. ½, ¼ ) |  |  |  |
| C3.3 | calculates using numbers expressed as whole numbers, fractions, decimals, percentages and integers |  |  |  |
|  | understands and uses properties of angles and triangles to solve problems |  |  |  |
|  | understands and uses formulas for finding the perimeter, area and volume of non-rectangular, composite shapes |  |  |  |
|  | chooses and performs required operations; makes inferences to identify required operations |  |  |  |
|  | selects appropriate steps to solutions from among options |  |  |  |
|  | interprets, represents and converts measures using whole numbers, decimals, percentages, ratios and fractions |  |  |  |
| D2 | selects and follows appropriate steps to complete tasks |  |  |  |
|  | locates and recognizes functions and commands |  |  |  |

This task:      was successfully completed___ 		needs to be tried again___

Learner Comments

____________________________						_________________________

#### Instructor (print)								Learner Signature